## Slide 1
Smart home
  Software simulation

## Slide 2
INTRO
UART
SERVO
LED
DC
LCD
Presentation content

## Slide 3
Communication Protocol
5 Features (Characteristics)
4 Pins
Represent The air condition
Using Lm35 as Temperature sensor
a type of electromechanical actuators
Controlled by PWM
3 wires
External Memory
16kbits (2kbytes)
I2C communications protocol
5 pins-self-timeted cycle: 5ms
frequency: 400kHz
Components

## Slide 4
Components
Each room has a LED as a source of light
Used in the alarm system
The alarm system protect the house from unauthorized person to access it by lighting the LEDs , Buzzer, etc…
electronic display module
Has 13 pins
can display 32 ASCII characters in two rows of 16 characters each Each of these rectangles is a grid of 5×8 pixels
Has two modes
have EIGHT TERMINALS. four are ROWS of MATRIX and four are COLUMNS of MATRIX.
These 8 PINS are driven out from 16 buttons present in the MODULE.

## Slide 5
UART & EEPROM|Controlling The System
01

## Slide 6
UART & EEPROM| Function
UART
  Used to communicate with the microcontroller
  Used as a main access to the system (Admin & User)
EEPROM
  Used to store the username & passwords of admins and users
  Used to store the crictial variables in the project

## Slide 7
UART & EEPROM| problems
UART
  How to make it the first priority for the system.
  The complicated connection with emergency case system.
EEPROM
  Searching for the Alternative to AT24C16A in Proteus.
  How to add and delete Admin/User.

## Slide 8
UART & EEPROM| problem solving
UART
  Using UART receive interrupt
  Using Key-Variables that make it easier to link
EEPROM
  Using Google & You-tube to search for Alternative and by trying many options
  Using Linked List method concept

## Slide 9
Servo Motor | SG90
02

## Slide 10
Servo Motor | Function
To control the door
Openning the door by +90 deg
Close the door by return to 0 deg

## Slide 11
Servo Motor | problems
Clock frequency
Duty cycle value
3. ICR1A value

## Slide 12
Servo Motor | problem solving
Using 16MHz as external clock so the timer will get 250kHz
Choose suitable value for ICR1A that gives period of 20ms (50Hz)
3. Choose suitable values for OCR1A

## Slide 13
LEDs & Alarm System
03

## Slide 14
LEDs & Alarm System | Function
LEDs are used to light each room separately ( 5 LEDs are independent )
Dimmer lamp with adjustable brightness which the user can control.
The Alarm System fires when a suspicious entry occurs on the LCD contol system turning on the LEDs and the Buzzer as an alert to the admin.

## Slide 15
LEDs & Alarm System | Problems
How to control the dimmer lamp brightness
How to isolate the LEDs and the dimmer lamp.
Connections of the buzzer & relay

## Slide 16
LEDs & Alarm System | Problem
Solving
Using PWM to convert the given brightness level into a variable voltage to the lamp
Using 4n25 transistor in order to isolate the circuits and avoid shorting them or damaging the ATMEGA 32
Using the same transistor in the connection of the buzzer and the relay made it easier & safer

## Slide 17
DC Motor | Tempreature control
04

## Slide 18
DC Motor | Function
Measures The Tempreature
If The Tempreature is > 28 ֯C The Air conditoner turns on“DC Motor“
If The Tempreature is < 21 ֯C The Air conditoner turns off“DC Motor

## Slide 19
DC motor | Problems
Sensing The Temperature
Sending The Temperature to motor
Turning The motor ON/OFF

## Slide 20
DC Motor| Problem solving
Using PWM in Timer 2
Using LM35 Temperature sensor
Choosing timer 2 pins and ADC pins to control the motor “ON/OFF Situation” when its necessary

## Slide 21
LCD & KEYPAD|emergancy case
05

## Slide 22
LCD & Keypad | Function
To control the system via keypad and LCD at emergancy cases(every thing except the door)
LCD shows each device working (including tempreture of the room)

## Slide 23
LCD & Keypad | Problems
Polling in case of the writing the code in main
Connections of KEYPAD
Limitation of the words that can fit the LCD

## Slide 24
LCD & Keypad| Problem Solving
Using external interrupt to avoid polling
Choosing pins far from timer pins ,ADC… that are in sequence to avoid the logical error